Siemens Hipath 4000 required Commands

Below is a personal document of Manish Kumar Sahdev and should not be downloaded and used without prior permission.

After opening COMWIN, press “Ctrl + T”. or press LOGON key.(Green color.)

LOGIN	= _root___

PASSW	= _hicom_

The LOGON message followed by “>” sign will appear on the screen.

This “>” is the command prompt to enter a valid command.

The screen is now divided in two windows.

The lower window is to enter commands & the output can be seen in the upper window.

(1)	To list the analog extension details

DIS-SCSU:	<CR>

STNO=     ;	<CR>		Extension Number

(2)	To change the COS of an analog extension

CHA-SCSU: 		<CR>

STNO= 		<CR>		Extension Number

DPLN= 		<CR>

ITR=			<CR>

COS1=		<CR>		Day time Class of Service

COS2=		<CR>		Night time/after locking Class of Service

LCOSV1=		<CR>		Day time Least Cost Routing COS

LCOSV2=	;	<CR>		Night time/after locking Least Cost Routing COS

(3)	To change the dialing type (DTMF/PULSE) for analog phone only.

CHA-SCSU:STNO=         	,DIAL=DTMF (For Tone instrument);<CR>

DP       	(For Pulse instrument);<CR>

(4)	To change the extension number

CHA-SCSU:STNO=        ,NEWNO=     ;<CR>

Pls. Note : for digital extensions the SCSU command is replaced by SBCSU.

(5)  To Deactivate an extension

DEA-DSSU: 		<CR>

OFFTYPE=DI		<CR>

TYPE=STNO		<CR>

STNO=  ;		<CR>		Extension Number

(6)  To Activate an extension

ACT-DSSU: 		<CR>

ONTYPE=AUL	<CR>

TYPE=STNO		<CR>

STNO=	  ;	<CR>		Extension Number

(7)  To see the name for a particular or all extensions

DIS-PERSI:		<CR>

TYPE=NAME	<CR>

STNO=	;	<CR>		Here if you give an extension number, the system

Will provide the name for that extension. If you do not give any number,

then system will list all the names entered in the system

(8)	To see the particular / all locking code(s) programmed in the system

DIS-PERSI:		<CR>

TYPE=STN		<CR>

STN=		   ;	<CR>		Enter the Extension number or omit to see all

the PINs  entered in the system.

OR

DIS-PERSI:		<CR>

TYPE=PIN		<CR>

PIN=		   ;	<CR>		Enter the PIN number or omit to see all

the PINs  entered in the system.

(9)	 To add the locking code / PIN for an extension

ADD-PERSI:		<CR>

TYPE=STN		<CR>

STNO=		<CR>		Extension Number

NAME=	   	<CR>		Do not give anything here

ORG=			<CR>		Do not give anything here

PINC=			<CR>		Do not give anything here

COSXCD=	    ;	<CR>		Give four digit PIN number

NOTE: Locking PIN and Mobile PIN are different feature but both the codes are same

(10) To display date and time of the system

DIS-DATE;		<CR>

(11)  To change date and time of the system

CHA-DATE:		<CR>

YEAR=		<CR>		4-digit year

MONTH=		<CR>		2-digit month

DAY=			<CR>		2-digit date

HOUR=		<CR>		2-digit hour in 24 Hr. format

MINUTE=		<CR>		2-digit minute

SECOND=	      ;	<CR>		2-digit second

(12)	To update system Hard Disk (HDD), save settings

EXE-UPDAT: A1, ALL;	<CR>

EXE-UPDAT: BP, ALL;	<CR>		Give this command twice.

Finally press LOGOFF key & close COMWIN.